## Slide 1
Crowd Supply
Course Workbook

## Slide 2: Table of Contents
About this Workbook | Slide 3
Pre-Lab: Workshop Pre-requisites | Slide 4
Lab : Implementing the Vivado Design | Slide 7

## Slide 3: About this Workbook
This workbook is designed to be used in conjunction with the Crowd Supply lab one workshop.
The contents of this workbook are created by Adiuvo Engineering & Training, Ltd.
If you have any questions about the contents, or need assistance, please contact Adam Taylor at adam@adiuvoengineering.com.

## Slide 4: Pre-Lab Workshop Pre-requisites

## Slide 5: Required Hardware
Pre-Lab
The following hardware is required to complete this series of labs
Digilent Basys3 Development board

## Slide 6: Downloads and Installations
Vitis 2020.2 – Includes Vivado | Download
Source Project Files | Download
Pre-Lab
Step 1 – Download and install the following at least one day prior to the workshop. This may take a significant amount of time and drive space.

## Slide 7: Lab Creating Pong on the Basys3

## Slide 8: Crowd Supply: Lab One
Step 1 – Open Vivado 2020.2. Once Vivado opens, open the Xhub Store
Lab One

## Slide 9: Crowd Supply: Lab One
Step 2 – Once the Xhub Stor Opens on the boards tab ensue Basys3 board is installed, right click to install
Lab One

## Slide 10: Crowd Supply: Lab One
Step 3 – When the Basys3 board is installed a green check will appear next to the board. Click close
Lab One

## Slide 11: Crowd Supply: Lab One
Step 4 – Create a new project, in the dialog which follows enter a Project name and location click next
Lab One

## Slide 12: Crowd Supply: Lab One
Step 5 – On the next tab, select RTL Project and check “do no specify sources at this time”, click next
Lab One

## Slide 13: Crowd Supply: Lab One
Step 6 – On the next tab select the Basys3 board and click next
Lab One

## Slide 14: Crowd Supply: Lab One
Step 7 – On the project summary page click finish
Lab One

## Slide 15: Crowd Supply: Lab One
Step 8 – When the project opens from IP Integrator select “Create Block Design”
Lab One

## Slide 16: Crowd Supply: Lab One
Step 9 – Leave the defaults in the dialog box which appears, click OK
Lab One

## Slide 17: Crowd Supply: Lab One
Step 10 – Once the Block Design is created select the board tab and drag the system clock onto the block design
Lab One

## Slide 18: Crowd Supply: Lab One
Step 11 – From the board tab drag the Reset signal on to the Clock Wizard Reset Pin
Lab One

## Slide 19: Crowd Supply: Lab One
Step 12 – Double click on the clock wizard and select CLK1 = 20 MHz, CLK2 = 25MHz, CLK3 = 50MHz
Lab One

## Slide 20: Crowd Supply: Lab One
Step 13 – Click on the + symbol and add a MicroBlaze to the block design
Lab One

## Slide 21: Crowd Supply: Lab One
Step 14 – Run the Block Automation and set the local memory to 128KB and ensure the Peripheral AXI Port is enabled
Lab One

## Slide 22: Crowd Supply: Lab One
Step 15 – This will create the MicroBlaze System as shown below. From the board tab drag the USB UART on to the block design.
Lab One

## Slide 23: Crowd Supply: Lab One
Step 16 – From the boards tab drag and drop the 4 Push Buttons onto block diagram
Lab One

## Slide 24: Crowd Supply: Lab One
Step 17 – Double click on the GPIO IP Block and re-customize it for a second channel of all outputs and width of 16 bits
Lab One

## Slide 25: Crowd Supply: Lab One
Step 18 – Run the Connection Automation and connect the UART and GPIO S_AXI interfaces to the MicroBlaze
Lab One

## Slide 26: Crowd Supply: Lab One
Step 19 – Open a web browser and clone the IP files from the GitHub https://github.com/ATaylorCEngFIET/Crowd SupplyWorkShop1
Lab One

## Slide 27: Crowd Supply: Lab One
Step 20 – This will clone three files one RTL File, a XDC constraints and an HLS IP core
Lab One

## Slide 28: Crowd Supply: Lab One
Step 21 – Click on the Add or Create design sources tab and then next
Lab One

## Slide 29: Crowd Supply: Lab One
Step 22 – Select the Seven_seg.vhd RTL file
Lab One

## Slide 30: Crowd Supply: Lab One
Step 23 – Create an RTL Wrapper for the block diagram, by right clicking on the block diagram icon. In the dialog which pops up let Vivado Manage the wrapper. Click OLK
Lab One

## Slide 31: Crowd Supply: Lab One
Step 24 – Drag the Seven Seg RTL block onto the block diagram and connect the second output port from the GPIO IP to the input of the Seven Segment Input
Lab One

## Slide 32: Crowd Supply: Lab One
Step 25 – Connect the clock of the Seven Segment to clock 1 (20 MHZ) and make the two ports external – Name them seven_seg & seven_seg_led_an
Lab One

## Slide 33: Crowd Supply: Lab One
Step 26 – Open the IP library, right click and select add repository – Select the Cloned Repository as the location
Lab One

## Slide 34: Crowd Supply: Lab One
Step 27 – This will add one repository to the project as shown by the dialog, click OK
Lab One

## Slide 35: Crowd Supply: Lab One
Step 28 – Right click on the user repository and select add IP to repository
Lab One

## Slide 36: Crowd Supply: Lab One
Step 29 – Select the zip in the cloned directory
Lab One

## Slide 37: Crowd Supply: Lab One
Step 30 – Under the User Repository you should now see the HUD IP Block
Lab One

## Slide 38: Crowd Supply: Lab One
Step 31 – Float the block diagram and maximize the window
Lab One

## Slide 39: Crowd Supply: Lab One
Step 32 – Use the + Symbol to add in the Test Pattern Generator, Video Mixer and HUD
Lab One

## Slide 40: Crowd Supply: Lab One
Step 33 – Double click on the Video Mixer and configure it as below
Lab One

## Slide 41: Crowd Supply: Lab One
Step 34 – Double click on the Test Pattern Generator and configure it as below
Lab One

## Slide 42: Crowd Supply: Lab One
Step 35 – Connect the Test Pattern Generator to the Stream Video in on the Video Mixer
Lab One

## Slide 43: Crowd Supply: Lab One
Step 36 – Connect the HUD OP to Stream AXIS Video 1 on the Video Mixer
Lab One

## Slide 44: Crowd Supply: Lab One
Step 37 – Run the connection automation and for all three modules select the clock wizard OP3 50MHz
Lab One

## Slide 45: Crowd Supply: Lab One
Step 38 – Check the Clock network to the HUD, TPG and Vmixer and AXI Network are 50MHz
Lab One

## Slide 46: Crowd Supply: Lab One
Step 39 – Use the + button to add in a Video Timing Generator and Constant block
Lab One

## Slide 47: Crowd Supply: Lab One
Step 40 – Double click the Video Timing Controller on it to re-customise – as shown below
Lab One

## Slide 48: Crowd Supply: Lab One
Step 41 – Run the connection automation to connect the VTC into the AXI Network – Ensure the clock is Clock 1 20MHz
Lab One

## Slide 49: Crowd Supply: Lab One
Step 42 – Add in a AXI Stream to Video Out IP block
Lab One

## Slide 50: Crowd Supply: Lab One
Step 43 – Double click to re-cusomtise the AXI Stream to video out block and configure it as below
Lab One

## Slide 51: Crowd Supply: Lab One
Step 44 – Connect the Vtiming Out to the Vtiming In of the VTC and AXIS to Video Out
Lab One

## Slide 52: Crowd Supply: Lab One
Step 45 – Connect the output of the Video Mixer to the AXIS Video Out Input
Lab One

## Slide 53: Crowd Supply: Lab One
Step 46 – Connect the clock out 3 to the aclk of the AXIS Video Out IP Block
Lab One

## Slide 54: Crowd Supply: Lab One
Step 47 – Connect the constant block to the VTC clken & SAXI_aclk_en and aclken & vid_io_out_ce on the AXIS video out
Lab One

## Slide 55: Crowd Supply: Lab One
Step 48 – Connect vtg_ce to gen_clken
Lab One

## Slide 56: Crowd Supply: Lab One
Step 49 – Connect sof_state_out to sof_state
Lab One

## Slide 57: Crowd Supply: Lab One
Step 50 – Connect Clock 2 (25MHz) to the clk of the VTC and vid_io_out_clk on the AXIS video out
Lab One

## Slide 58: Crowd Supply: Lab One
Step 51 – Click on regenerate layout to make the diagram more understandable
Lab One

## Slide 59: Crowd Supply: Lab One
Step 52 – Expand the vid_io_out on the AXIS Video Out block
Lab One

## Slide 60: Crowd Supply: Lab One
Step 53 – Make the Vid_hsync external and re-name it Hsync
Lab One

## Slide 61: Crowd Supply: Lab One
Step 54 – Make the Vid_vsync external and re-name it Vsync
Lab One

## Slide 62: Crowd Supply: Lab One
Step 55 – Add in three slices and connect them to the Vid_data output
Lab One

## Slide 63: Crowd Supply: Lab One
Step 56 – Re-customize Slice 0 with the settings as below
Lab One

## Slide 64: Crowd Supply: Lab One
Step 57 – Re-customize Slice 1 with the settings as below
Lab One

## Slide 65: Crowd Supply: Lab One
Step 58 – Re-customize Slice 2 with the settings as below
Lab One

## Slide 66: Crowd Supply: Lab One
Step 59 – Make the Three Slice outputs external name them Slice0 vgaRed, Slice1 vgaBlue and Slice2 vgaGreen
Lab One

## Slide 67: Crowd Supply: Lab One
Step 60 – Add in a New processor reset block and connect its clock input to clock 2
Lab One

## Slide 68: Crowd Supply: Lab One
Step 61 – Connect the DCM locked signal
Lab One

## Slide 69: Crowd Supply: Lab One
Step 62 – Connect the Reset signal to the ext_reset_in of the new processor reset block
Lab One

## Slide 70: Crowd Supply: Lab One
Step 63 – Connect the peripheral_aresetn from the reset block to the VTC resetn
Lab One

## Slide 71: Crowd Supply: Lab One
Step 64 – Connect the peripheral_areset from the reset block to the AXIS Video Out vid_in_out_reset
Lab One

## Slide 72: Crowd Supply: Lab One
Step 65 – Connect the peripheral_areset from the reset block associated with the clock 3 (50 Mhz) with the AXIS Video out aresetn input
Lab One

## Slide 73: Crowd Supply: Lab One
Step 66 – Validate the design, we should see no errors or warnings
Lab One

## Slide 74: Crowd Supply: Lab One
Step 67 – Add in a new constraints source and select the IO constraints from the github repo
Lab One

## Slide 75: Crowd Supply: Lab One
Step 68 – The final block design should look as below
Lab One

## Slide 76: Crowd Supply: Lab One
Step 69 – Click on build the bit stream – If you see the following dialog select yes
Lab One

## Slide 77: Crowd Supply: Lab One
Step 70 – Click on build the bit stream – select the number of jobs and click run
Lab One